## Slide 1: Lecture 18
Queuing Models

## Slide 2: Queuing Models
A manufacturing plant: system with machines, people, etc.
A bank or other service operations, with different kinds of customers, servers, teller windows, ATMs, safe deposit boxes.
A computer network with servers, clients, storage space (HDs), printers, networking capabilities, and operators.
A supermarket or chain-store with inventory control, check-outs, and customer services.
A chemical products plant with storage tanks, pipeline, reactor vessels, and railway tanker cars that ship the finished goods.

## Slide 3: Characteristics of a Queuing System
The queuing system is determined by:
Arrival characteristics
Queue characteristics
Service facility characteristics

## Slide 4: Arrival Characteristics
Size of the arrival population – either infinite or limited
Arrival distribution:
  Either fixed or random
  Either measured by time between consecutive arrivals, or arrival rate
  The Poisson distribution is often used for random arrivals

## Slide 5: Poisson Distribution
λ = the average arrival rate per time unit
P(x) = the probability of exactly x arrivals occurring during one time period
P(x) = e-λ λx
x!

## Slide 6: Behavior of Arrivals
Most queuing formulas assume that all arrivals stay until service is completed
Balking refers to customers who do not join the queue
Reneging refers to customers who join the queue but give up and leave before completing service

## Slide 7: Queue Characteristics
Queue length (max possible queue length) – either limited or unlimited
Service discipline
  Usually FIFO (First In First Out)
  LIFO (Last In First Out)
  Priority queues
  Random

## Slide 8: Service Facility Characteristics
Configuration of service facility
  Number of servers (or channels)
  Number of phases (or service stops)
Service distribution
  The time it takes to serve 1 arrival
  Can be fixed or random
  Exponential distribution is often used

## Slide 9: Measuring Queue Performance
ρ = utilization factor (probability of all
servers being busy)
Lq = average number in the queue
L = average number in the system
Wq = average waiting time
W = average time in the system
P0 = probability of 0 customers in system
Pn = probability of exactly n customers in system

## Slide 10: Kendall’s Notation
A / B / s
A = Arrival distribution
    (M for Poisson, D for deterministic, and G for general)
B = Service time distribution
(M for exponential, D for deterministic, and G for general)
S = number of servers

## Slide 11: Models Covered
Name (Kendall Notation) | Example
Simple system (M / M / 1) | Customer service desk in a store
Multiple server (M / M / s) | Airline ticket counter
Constant service (M / D / 1) | Automated car wash
General service (M / G / 1) | Auto repair shop
Limited population (M / M / s / ∞ / N) | An operation with only 12 machines that might break

## Slide 12: Single Server Queuing System (M/M/1)
Poisson arrivals
Arrival population is unlimited
Exponential service times
All arrivals wait to be served
λ is constant
μ > λ (average service rate > average arrival rate)
Have we seen this before?

## Slide 13: Operating Characteristics for M/M/1 Queue
Average server utilization
ρ = λ / μ
Average number of customers waiting
  Lq = λ2
  μ(μ – λ)
Average number in system
L = Lq + λ / μ

## Slide 14
Average waiting time
Wq = Lq = λ
λ μ(μ – λ)
Average time in the system
  W = Wq + 1/ μ
Probability of 0 customers in system
P0 = 1 – λ/μ
Probability of exactly n customers in system
Pn = (λ/μ )n P0

## Slide 15: Single Server Queuing System (M/M/1/K)
Poisson arrivals
Arrival population is unlimited
Exponential service times
All arrivals wait to be served
λ is constant
μ > λ
System can hold a maximum capacity of K
Have we seen this before?