## Slide 1: Lecture 22
Simulation

## Slide 2: What’s Simulation?
“ Imitation of the operation of a real-world process or system over time”
  Very popular and powerful method
  Applies in many fields and industries
  Rides the wave of evolving computing technology

## Slide 3: Modeling
Simulation involves two major parts:
  Systems and,
  Models of them
Models:
  Descriptive models: process flow chart
  Queuing models
  And many more

## Slide 4: Examples:
A manufacturing plant: system with machines, people, transportation devices, storage spaces.
A distribution network of plants, warehouses, and transportation links.
A bank or other service operations, with different kinds of customers, servers, teller windows, ATMs, safe deposit boxes.
A computer network with servers, clients, storage space (HDs), printers, networking capabilities, and operators.
A supermarket or chain-store with inventory control, check-outs, and customer services.
A chemical products plant with storage tanks, pipeline, reactor vessels, and railway tanker cars that ship the finished goods.

## Slide 5: Why simulation?
Why not just use the system?
When you cannot play with the system
  Flight simulators
  Logical (or mathematical) models

## Slide 6: Computer Simulation
Model of real-life systems
  numerical evaluation using software
Specially useful on complex systems, where mathematical models are not easy or not possible to build.

## Slide 7: Pros and Cons
Pros:
  Easy to build for large & complex systems
  Efficiently evaluate what-if solutions
  Model building process and results are straight-forward and easy to understand
Cons:
  Time consuming for computer resources, rely on good computing power
  Results are based on random input and stochastic processes

## Slide 8: Simulation Fundamental Concepts
An Example system
Drilling Machine Center
Drill table
Finished parts
Waiting line
Arrival parts
Part in process

## Slide 9: Model Specifics
Initially (time 0) empty and idle
Base time units: minutes
Input data (assume given for now …), in minutes:
Part Number Arrival Time Interarrival Time Service Time
1 0.00 1.73 2.90
2 1.73 1.35 1.76
3 3.08 0.71 3.39
4 3.79 0.62 4.52
5 4.41 14.28 4.46
6 18.69 0.70 4.36
7 19.39 15.52 2.07
8 34.91 3.15 3.36
9 38.06 1.76 2.37
10 39.82 1.00 5.38
11 40.82 . .
. . . .
. . . .
Stop when 20 minutes of (simulated) time have passed

## Slide 10: The objectives:
The total production (# of parts that completed) during 20 minutes period
Average waiting time in queue
The maximum time waiting in queue
The time-average number of parts in queue Q(t)
Average and maximum total time in the system
Utilization of the drilling machine

## Slide 11: Simulation Clock
The current time of simulation is simply held in a variable call the simulation clock “TNOW”
Unlike the real time, the simulation clock does NOT flow continuously
It lurches from time to time when event happened.
The simulation clock interacts closely with the event calendar.

## Slide 12: Simulation by Hand
Manually track state variables, statistical accumulators
Use “given” interarrival, service times
Keep track of event calendar
“Lurch” clock from one event to the next
Will omit times in system, “max” computations here (see text for complete details)

## Slide 13: Simulation by Hand: Setup
# of servers busy (time t)
# in queue (time t)

## Slide 14: Model Specifics
Initially (time 0) empty and idle
Base time units: minutes
Input data (assume given for now …), in minutes:
Part Number Arrival Time Interarrival Time Service Time
1 0.00 1.73 2.90
2 1.73 1.35 1.76
3 3.08 0.71 3.39
4 3.79 0.62 4.52
5 4.41 14.28 4.46
6 18.69 0.70 4.36
7 19.39 15.52 2.07
8 34.91 3.15 3.36
9 38.06 1.76 2.37
10 39.82 1.00 5.38
11 40.82 . .
. . . .
. . . .
Stop when 20 minutes of (simulated) time have passed

## Slide 15: Simulation by Hand: t = 0.00, Initialize

## Slide 16: Simulation by Hand: t = 0.00, Arrival of Part 1
1

## Slide 17: Simulation by Hand: t = 1.73, Arrival of Part 2
1
2

## Slide 18: Simulation by Hand: t = 2.90, Departure of Part 1
2
= 2.90 (clock time)
– 1.73 (arrival of 2)

## Slide 19: Simulation by Hand: t = 3.08, Arrival of Part 3
2
3

## Slide 20: Simulation by Hand: t = 3.79, Arrival of Part 4
2
3
4

## Slide 21: Simulation by Hand: t = 4.41, Arrival of Part 5
2
3
4
5

## Slide 22: Simulation by Hand: t = 4.66, Departure of Part 2
3
4
5

## Slide 23: Simulation by Hand: t = 8.05, Departure of Part 3
4
5

## Slide 24: Simulation by Hand: t = 12.57, Departure of Part 4
5

## Slide 25: Simulation by Hand: t = 17.03, Departure of Part 5

## Slide 26: Simulation by Hand: t = 18.69, Arrival of Part 6
6

## Slide 27: Simulation by Hand: t = 19.39, Arrival of Part 7
6
7

## Slide 28: Simulation by Hand: t = 20.00, The End
6
7

## Slide 29: Simulation by Hand: Finishing Up
Average waiting time in queue:
Time-average number in queue:
Utilization of drill press: